## Slide 1: Analytical Walking Models + RL towards Less Painful Biped Walking Policies
Noah Fisher and Daniel Levine

## Slide 2: Training walking policies is hard and opaque for model free. Creating walking controllers is tedious and often fragile using classical methods. Can we create a classical foundation for baseline ability, and use RL to provide robustness?

## Slide 3: To Answer This Question:
Linear Dynamics Models for Walking
Quadratic Cost
Closed Form Expressions  Derive LQR Baselines
Introduce Unmodelled Noise
Train (Ideally) Using Structure but with perturbations
Compare Baseline Analytic Controllers to RL Policies (in progress)

## Slide 4: Our Linear Template Models: LIP, 3LP
3LP, Faraji 2015
LIP, Kajita 1991
3LP is a three linearized pendulum extension for swing dynamics.

## Slide 5: 3D LIP

## Slide 6: LIP Dynamics

## Slide 7: Generating a Walking Pattern
Notes: By defining step size, single support period, and the orbital energies, we can compute a stable periodic walking pattern!

## Slide 8: However, the Trajectories are Unstable Equilibriums
Notes: However, much like a ball sitting at the top of a hill, these walking patterns become unstable with the slightest of nudges

## Slide 9: Closing the Loop Part 1: Discretization (ZOH)
Notes: State Space → ZOH Discretization. A, B come from linear dynamics

## Slide 10: Closing the Loop Part 2: LQR and the Riccati

## Slide 11: Our Gait is Stable for Random Disturbances!
Notes: Footstep error (unknown to controller) generated via gaussian noise

## Slide 12: But NOT Stable for Noisy Footsteps :(

## Slide 13: Problem: We don’t observe footstep error, and it’s difficult to model Solution: Use RL to compute a residual for foot placement!
RL!

## Slide 14: LIP RL Setup
Goal:
Robustly track reference trajectory even noisy steps
State:
reward
Defined using error coordinates from ref gait
Action:

## Slide 16: 3LP

## Slide 17: 3LP Dynamics
Model
Linear! (but ugly)
3 Linear Pendulums
Constant and ramped ankle and hip torques
Closed form solution for gait gen and control
Notes: Cite faraji for the dynamics

## Slide 18: Two Phases: Hybrid Model → Total Stride Map
Total Stride Map (closed form dynamics)
If stable,
always look the same
Apply a Foot Swap and Centering “Reset” matrix to make every cycle appear the same math-wise.
Notes: https://www.researchgate.net/figure/A-Poincare-Map-is-used-to-find-walking-solutions-and-to-analyze-stability_fig1_322069775

## Slide 19: Use the Stride Map + Nullspace Conditions for Reference Gait
For Symmetric, Periodic Gait, Solve for Limit Cycle over 2 Full Strides (L,R,L)
Write out the double stride map
2. Solve limit cycle torques for double stride map via null space equations:
Periodicity - Rel Pos of limbs are the same at boundaries
Symmetry - Swing foot has zero vel relative to stance foot at impact
No Slip - Stance foot must have zero vel

## Slide 20: Use the Stride Map + Nullspace Conditions for Reference Gait
Null Space Solve:
And then we solve a QP to select the minimum energy gait to achieve the target speed, ds and ss parameters.

## Slide 21: Reference Gait Generation From Selected Nullspace Criteria
Speed:0.4 m/s
Step Time: 0.1s ds, 0.6s ss
Speed:1.2 m/s
Step Time: 0.1s ds, 0.6s ss

## Slide 22: DLQR and Time Projection Controller
DLQR - Correction Once Per Stride
Standard discrete LQR procedure, using the stride map dynamics (reduced state to moving pelvis and foot via M).
Solved via fixed point iteration due to repeated eigenvalues. Decomposition methods numerically fail.
As we are stabilizing the poincare map, this is once per stride.
DLQR + Time Projection – Run it back!
Extension of LQR for continuous control by projection of error to boundary for DLQR (Faraji 2017)

## Slide 23: Open Loop vs. DLQR Time Proj. 5 cm Perturbation
Open Loop (1.2m/s)
Time Projection DLQR (1.2m/s)

## Slide 24: OK! Stabilizing 3LP is not hopeless.

## Slide 25: 3LP RL Setting On Policy Stochastic Actor Critic, TD(0)

## Slide 26: 3LP RL Setting
State:
Actions:
Small change torques applied to hip and ankle
Transition Dynamics:
(Designed for Actor Critic)

## Slide 27: Parameterization for Actor Critic
Originally Designed for Stride Level Control – But using linear controllers could not stabilize using DLQR alone  aimed to use policy w/more frequent actions
State Error Coordinates Relative to Reference Trajectory:
Actor Parameterization: Linear Combination of Error Coordinates  Linear state feedback policy

## Slide 28: Critic Parameterization: Linear Combination of Quad Monomials
Critic Parameterization: Linear Combination of Quadratic Monomials
Using error coordinates z_k as for actor parameterization:

## Slide 29: Reward (Cost) Function and Termination
Reward: Formulate like negative LQR Cost
Termination: ”Fall”
Pelvis moves too far from stance foot
Pelvis velocity exceeds a threshold
Large discrete negative reward

## Slide 30: In practice – AC stalled, PPO

## Slide 31: In progress – but PPO also stalled

## Slide 32: Residuals and Torques Looks Reasonable, But Policy is Poor

## Slide 33: Residuals and Torques Looks Reasonable, But Policy is Poor

## Slide 34: Conclusions

## Slide 35: Insights
Even with all the structure we built up, for walking in this precise manner – learning residuals was still not easy. The unstable system wants to be unstable. This was surprising.
LQR, even for a difficult Poincare-map system, works decently (though also a bit fragile)
If for a linear system LQR doesn’t work – likely RL won’t either. (RL is LQR!)
For all the cleverness with linear combinations – MLP’s and PPO seem just as good.
We want the RL part to really work for the report!

## Slide 36: Lastly,
We had fun and learned a lot!
Thanks all!

## Slide 37: Sources
Kajita, S. (2017). Linear inverted pendulum-based gait. In Humanoid robotics: A reference (pp. 1-18). Springer, Dordrecht.
Faraji, S., & Ijspeert, A. J. (2017). 3LP: A linear 3D-walking model including torso and swing dynamics. the international journal of robotics research, 36(4), 436-455.
Faraji, S., & Ijspeert, A. J. (2016). A new time-projecting controller based on 3LP model to recover intermittent pushes. arXiv preprint arXiv:1605.03039.